## Slide 1: Data-Driven Methods in Image Processing
CMPUT 206
Nilanjan Ray

## Slide 2: What is a data-driven method?
I don’t think there is a rigorous definition!
Loosely speaking, if an algorithm relies on a lot of data during run-time to accomplish a task, it is referred to as a data-driven method
In the next few lectures, we will study some examples:
  De-noising
  Texture synthesis
  Super resolution
  Image inpainting
  Object removal

## Slide 3: De-noising
We will first study a famous de-noising method called bilateral filter
Next, we will study a method called non-local means which is a generalization of bilateral filter
Finally, we will take a look at BM3D method

## Slide 4: Bilateral filtering setup
Let I and J be the input and output of the bilateral filtering, respectively.
Let (i, j) denote a pixel location.
Let N(i, j) denote set of neighboring pixels of (i, j); Note, N(i, j) includes pixel (i, j) as well.
Let w((i, j), (m, n)) denote non-negative weight assigned to pixel pairs (i, j) and (m, n).
How do we create this weights? Relationship with Gaussian filtering?

## Slide 5: Bilateral filtering
In comparison, Gaussian filter weights are independent of gray/color values:
Weight depends
on gray/color values

## Slide 6: Bilateral filtering examples
Input image
Gaussian filter
bilateral filter
Bilateral filter is able to preserve edges; but Gaussian filter failed; why?

## Slide 7: Why Gaussian filter cannot preserve edges?
*
=
edge pixel
edge pixel gray value diminished!
Weighted average
operation
Input
Output

## Slide 8: Why bilateral filter preserves edges?
x
*
=
edge pixel
Almost no change at edge pixel!

## Slide 9: Bilateral filter weights in 2D
input
Wc
Ws
Ws*Wc
Output
Slide source: http://faculty.cs.tamu.edu/jchai/csce441_2015fall/

## Slide 10: Nonlocal means filtering
Let us denote input image by I and output image by J, as before
For every pixel location (i, j), consider a small image patch around it; call it Pi, j
Find out similar patches Pm, n centered at pixel locations (m, n)
Consider weight between (i, j) and (m, n) as
  W(i, j), (m, n) = exp(-||Pi, j - Pm, n||2/s), s is a user input parameter
Output image is calculated by
As we can see here that the mean is a weighted non-local mean

## Slide 11: NL means filtering…
w(p, q1) and w(p, q2) would be large
w(p, q3) would be small
Source: A. Buades, B. Coll and J. M. Morel, "A non-local algorithm for image denoising," Computer Vision and Pattern Recognition, 2005. CVPR 2005. IEEE Computer Society Conference on, 2005, pp. 60-65 vol. 2. doi: 10.1109/CVPR.2005.38

## Slide 12: NL filtering result with some comparisons
Source: A. Buades, B. Coll and J. M. Morel, "A non-local algorithm for image denoising," Computer Vision and Pattern Recognition, 2005. CVPR 2005. IEEE Computer Society Conference on, 2005, pp. 60-65 vol. 2. doi: 10.1109/CVPR.2005.38

## Slide 13: BM3D: Block matching and collaborative filtering
Picture source: http://www.cs.tut.fi/~foi/GCF-BM3D/BM3D_TIP_2007.pdf

## Slide 14: Grouping by Block Matching
For every noisy reference block:
  Calculate SSD between noisy blocks
  If SSD<thr add to group
Picture source: http://www.cs.tut.fi/~foi/GCF-BM3D/BM3D_TIP_2007.pdf

## Slide 15: 3D transform + collaborative filtering
Apply wavelet transform to 3D blocks
Apply hard thresholding to wavelet coefficients
Apply inverse wavelet transform to obtain de-noised 3D blocks

## Slide 16: Fusion of de-noised 3D blocks
Blocks are merged by suitable weights obtained from previous filtering steps

## Slide 17: BM3D examples
Picture source: http://www.cs.tut.fi/~foi/GCF-BM3D/BM3D_TIP_2007.pdf

## Slide 18: Deep learning-based denoising
https://arxiv.org/pdf/1608.03981.pdf
Deep learning achieves state-of-the-art results in image denoising today!

## Slide 19: Next lecture
Data-driven texture synthesis